## Slide 1: Bio-Bitumen Plant Project — 25 TPD
Prepared for: Rajesh
By: PPS Anantams
Date: 07 April 2026
Location: Ahmedabad, Gujarat

## Slide 2: Project Overview
Technology: Biomass Pyrolysis (CSIR-CRRI Licensed)
Capacity: 25 TPD agro-waste feed
Investment: Rs 10.00 Crore
Location: Ahmedabad, Gujarat
Products: Bio-Bitumen VG30/VG40, Bio-Char, Bio-Oil, Carbon Credits

## Slide 3: Market Opportunity
India Bitumen Market: Rs 25,000+ Crore/year
Import Dependency: 49%
Plants Needed: 130-216 in next 5-7 years
NHAI Green Mandate: 15% bio-bitumen by 2030
CSIR-CRRI technology transferred to 14 companies (Jan 2026)

## Slide 4: Technology — CSIR-CRRI Licensed
Process: Biomass → Pyrolysis (500°C) → Bio-Oil + Char + Syngas
Yields: Bio-Oil 32% | Bio-Char 28% | Syngas 22%
Blend: 20% bio-oil in VG30 bitumen
Quality: Meets IS:73 VG30/VG40 specifications

## Slide 5: 13-Step Manufacturing Process
1. Biomass Receiving → 2. Shredding → 3. Drying
4. Pelletization → 5. Pyrolysis (450-550°C)
6. Bio-Oil Condensation → 7. Oil Storage
8. VG-30 Heating → 9. High Shear Blending
10. Quality Testing (IS:73) → 11. Product Storage
12. Drum/Tanker Packing → 13. Dispatch to NHAI/PWD

## Slide 6: Key Equipment — 15 Items
Reactor: 1x Ø1.5m × 4.5m
Dryer: Ø1.4m × 7.0m
Total Motor Load: 347.0 kW
SC-101: Weighbridge + Receiving Hopper — Weighbridge 18m×3.5m | Hopper 21m³
SZ-101: Primary Shredder / Chipper — 2800mm×1800mm×2200mm | Output: 50mm size
DR-101: Rotary Drum Dryer — Drum: Ø1.4m × 7.0m | 150°C | 3.5 RPM
GR-101: Secondary Grinder / Fine Hammer Mill — 2200mm×1400mm×1800mm | Input: 50mm → Output: 3mm |
PR-101: Pyrolysis Reactor (Rotary Kiln) — Ø1.5m × 4.5m | Wall: 12mm SS310S | Insulation: 100
CD-101: Shell & Tube Condenser — 4.5m × Ø0.8m | Cooling water: 12 m³/hr | Bio-oil o
BT-101: Bio-Oil Storage Tank (Atmospheric) — Ø3.3m × 2.6m | 28.8 m³ each | Shell 6mm, Roof 5mm
BIT-101: Conventional Bitumen Tank (Heated) — Heated to 160°C | Insulation 100mm + Al cladding |

## Slide 7: Bill of Quantities — 82 Items
Total BOQ: Rs 681 Lac (6.81 Cr)
Zones: 15
A. Gate & Security: Rs 16 Lac
B. RM Receiving: Rs 27 Lac
C. Pre-Processing: Rs 43 Lac
D. Reactor Zone: Rs 195 Lac
E. Oil Recovery: Rs 22 Lac
F. Blending: Rs 46 Lac
G. Storage: Rs 45 Lac
H. Packing & Dispatch: Rs 27 Lac

## Slide 8: Plant Layout — 120m × 80m
15 Zones: Gate → RM → Processing → Reactor → Oil → Blending → Storage → Dispatch → Electrical → Utilities → Lab → Safety → Civil → Office → Maintenance
Safety: 15m reactor clearance, 6m roads, 45m hydrant spacing

## Slide 9: Project Cost
Total Investment: Rs 10.00 Crore
Bank Loan (60%): Rs 6.00 Crore
Promoter Equity (40%): Rs 4.00 Crore
EMI: Rs 7.30 Lac/month
Interest Rate: 11.5% p.a.

## Slide 10: Revenue & Profitability
Revenue Year 5: Rs 815 Lac
Monthly Profit: Rs 5.0 Lac
ROI: 20.0%
IRR: 26.0%
Break-Even: 30 months
DSCR Year 3: 1.50x

## Slide 11: Compliance & Licenses
Key Approvals Required:
- CTE (Consent to Establish) — State PCB
- CTO (Consent to Operate) — State PCB
- Factory License — Factory Inspector
- Fire NOC — Fire Department
- PESO License — for petroleum storage
- GST Registration
- MSME Registration
Total: 25 licenses — We handle ALL

## Slide 12: Government Schemes & Subsidies
MNRE Biomass: 25% capital subsidy (max Rs 2.1 Cr)
State MSME: Varies by state
CGTMSE: Collateral-free up to Rs 5 Cr
Carbon Credits: Rs 328.1 Lac/year
NHAI Green Mandate: Priority procurement

## Slide 13: Project Timeline — 12 to 18 Months
Month 1: DPR + Feasibility
Month 1-2: Company Setup
Month 2-4: Land + Approvals
Month 3-7: Environmental Clearances
Month 3-5: Bank Loan
Month 5-8: Equipment Order
Month 6-10: Civil Construction
Month 10-12: Installation
Month 13+: Commercial Production

## Slide 14: Why PPS Anantams?
Experience: 25 years in bitumen industry
Plants Built: 10 across India
Network: 4,452 industry contacts
International: VG-30 supply 2.4 Lakh MT/yr
Turnkey: DPR to Dispatch — complete solution

## Slide 15: Next Steps
1. Finalize capacity and location
2. Sign consulting agreement
3. DPR generation (7 days)
4. Bank loan application
5. Site identification
6. Equipment procurement
7. Construction & commissioning
Contact: Prince Pratap Shah | +91 7795242424